Press Release

RAFI expands RAFIX 22 FS+ control components to include a compact emergency-stop pushbutton

Berg/Ravensburg – RAFI is expanding the RAFIX 22 FS+ control components to include a compact emergency-stop pushbutton with an installation height of only 25.9 mm from the front plate. The mushroom shape of the illuminated emergency-stop pushbutton and its snap-in contact connection when actuated prevents blockage of functionality due to jammed object or textiles. The latched-in position of the pushbutton can be reset by rotation.

Figure: The compact emergency-stop pushbutton from the RAFIX 22 FS+ Control Component Series

Just like all RAFIX 22 FS+ operating components, the compact emergency-stop pushbutton can also be combined with PCB solder terminal contact blocks (PCB) for PCB mounting or with quick-connect contact blocks (QC) for directly wired connection. The button has been designed for mounting holes with a diameter of 22.3 mm.

With the PCB solution, it reaches the low mounting depth typical of the RAFIX 22 FS+ , only 9.2 mm. Based on this, modern housing designs with a very flat construction can be implemented. To achieve this, contact blocks of this series are taken into consideration in PCB layouts and arranged next to other components. In this way, pushbuttons, keyswitches or selector switches from the RAFIX 22 FS+ series can be combined on the same printed circuit board with RAFI short-travel keyswitches in various dimensions and with various tactile switching forces and actuating areas. In contrast, the QC contact blocks with quick-connect terminals make especially quick and economical assembly possible. The pre-fabrication of the cable assemblies with contact blocks also makes everything especially easy due to the tool-free assembly principle. The mounting depth of the control components is 27 mm with the QC version. The compact emergency-stop pushbutton reaches IP 65 protection class from the front. The associated contact blocks are available in designs with two normally-closed contacts as well as with one normally-closed contact and one normally-open contact.

| Figures: | not-halt_kompakt | Char.s: | 1,804 |
| --- | --- | --- | --- |
| File name: | 201502049_pm_nothalt-kompakt_engl | Date: | 2015-02-19 |

Company background RAFI group

Founded in 1900, RAFI now develops and produces electromechanical components such as pushbuttons and switches, operating systems such as touch screens, keyboards, electronic components, and systems for man-machine communication. RAFI products are employed in more than 30 industries, e.g., in medical equipment, mechanical engineering, road and railway vehicles, household appliances, and telecommunications. The RAFI group operates internationally with approx. 2,000 employees at ten sites in Germany, Europe, China, and the USA. The group’s headquarters are located in Berg (Baden-Württemberg, Germany).

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Str. 128-134 88276 Berg Germany Tel.: +49 . 751 . 891 307 Fax: +49 . 751 . 891 300 e-mail: artur.krug@rafi.de WWW: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 . 30 . 5389 650 Fax: +49 . 30 . 5389 6529 e-mail: info@gii.de WWW: www.gii.de |
| --- | --- | --- |