Press Release

CONTA-CLIP expand industrial enclosure portfolio with ABS and polycarbonate boxes

Hövelhof – CONTA-CLIP expand their comprehensive industrial housing program with new ABS and polycarbonate terminal boxes. CG and CG-PC series housings come in 15 sizes ranging from 84 x 82 x 55 mm to 302 x 232 x 110 mm. ABS enclosures feature high resistance to seawater as well as UV stability and resistance to chemicals. They conform to flammability class HB (UL 94) and provide IP66/IP67 protection. The shock-resistant housings are suitable for temperatures ranging from -25 to +40 °C.

Figure 1: ABS and polycarbonate terminal boxes now complement CONTA-CLIP's enclosure portfolio

CG-PC type housings are suited for applications requiring even higher shock and temperature resistance: glass-fiber reinforced polycarbonate housings conform to the same protection class as CG series boxes, but are suitable for temperatures ranging from -35 °C to +80 °C and conform to shock resistance class IK 08 and flammability class V-2. Both series can be optionally fitted with opaque polystyrene covers or transparent polycarbonate covers. Both types  feature protected labeling indentations and can be fastened via quick locks. Another new housing series is the CK-PC line equipped with metric knockouts, which are specifically optimized for photovoltaic applications. CONTA-CLIP offers mounting rails of electro-galvanized steel in TS 15 and TS 35 sizes as well as mounting plates. To ensure quick installation and to facilitate cable entry, CONTA-CLIP provides the housings with various threaded holes and with metric knockouts on request. Further accessories include wall brackets for wall mounting and a great variety of cable gland systems. The enclosures are available in gray color (similar to RAL 7035). The “Housing system” catalog is available on CONTA-CLIP's website for PDF download or in print.

| Figures: | neue_abs_und_ pc -gehaeuse | Char.s: | 1791 |
| --- | --- | --- | --- |
| File name: | 201504008_pm_neue_gehaeuseserie_engl | Date: | 2015-07-14 |

Company Background

CONTA-CLIP is one of Europe’s leading manufacturers of electric terminal blocks. Based in Hövelhof, Germany, the medium-sized, family-run company has been producing electric and electronic connection systems for the process and automation industries for more than 30 years. CONTA-CLIP supplies all industry sectors, focusing on railroad industries, shipbuilding, building automation, conveyor technology, machine and plant engineering and construction, instrumentation and control technology, control panel manufacturing, transformer manufacturing, and environmental technology. The company consists of three specialized branches: CONTA-CONNECT for electric connection technology, CONTA-ELECTRONICS for electronics and CONTA-CON for PCB edge connectors. Additionally, CONTA-CLIP provides services such as customizing housings and mounting rails, labeling and supplying user-specific electronic components.

| Contact: CONTA-CLIP Verbindungstechnik GmbH Christian Quade Otto-Hahn-Str. 7 33161 Hövelhof Germany tel.: +49 . 52 57 . 98 33 - 0 fax: +49 . 52 57 . 98 33 - 33 email: quade@conta-clip.de WWW: www.conta-clip.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany tel.: +49 . 30 . 53 89 65 - 0 fax: +49 . 30 . 53 89 65 - 29 email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |