Press Release

New space saving FRK PushIN terminal blocks from CONTA-CLIP come in 3-pole and double level versions

Hövelhof – CONTA-CLIP's PushIN installation terminals are now available in two new, space-saving versions with more connection options. The new feed-through terminal FRKI  6-10/3A features three connectors for large wire cross sections of up to 10  mm² and a rated current of 57 A.

Illustration 1: More options for connection: new feed-through terminal FRKI 6-10/3A and  protective earth terminal FSLI

For potential distribution via adjoining terminals, the 3-pole terminal is equipped with inboard cross connection channels for 2-10 pole connection with the cross connection system FIQI 6-10. Like all CONTA-CLIP terminals, the FRK series allows for easy wire contacting without tools, thanks to the PushIN pressure-spring connection system. A double level version, FRKD 2.5/3A, is also available: at a width of only 5 mm, it features six connectors for wire cross sections up to 4 mm². The feed-through terminal comes with 2x3 or 1x6 connectors for a rated current of 24 A. The pluggable potential distribution system FQI 2.5 can be used to cross-connect potentials of the upper and lower level.

Illustration 2: Double level terminals FRKD 2,5/3A and FSLD

Both new terminal types, FRKI 6-10/3A and FRKD 2.5/3A, are also available as protective earth terminals FSLI and FSLD respectively. The PE foot of these terminals makes contact on both sides and safely connects the PE potential to the mounting rail. The foot segment and bus bar are made from copper. This choice of material ensures a low transition resistance and a high level of safety for the automatic spring-action protective earth PE foot. The terminal housing material is PA 6.6 V0 suitable for a temperature range of -40°C to +120°C.

| Illustrations: | f rki3a_fsli3a frkd3a_fsld3a | Char.s: | 1685 |
| --- | --- | --- | --- |
| File name: | 201506012_pm_frki3a_frkd3a | Date: | 2015-07-14 |

Company Background

CONTA-CLIP is one of Europe’s leading manufacturers of electric terminal blocks. Based in Hövelhof, Germany, the medium-sized, family-run company has been producing electric and electronic connection systems for the process and automation industries for more than 30 years. CONTA-CLIP supplies all industry sectors, focusing on railroad industries, shipbuilding, building automation, conveyor technology, machine and plant engineering and construction, instrumentation and control technology, control panel manufacturing, transformer manufacturing, and environmental technology. The company consists of three specialized branches: CONTA-CONNECT for electric connection technology, CONTA-ELECTRONICS for electronics and CONTA-CON for PCB edge connectors. Additionally, CONTA-CLIP provides services such as customizing housings and mounting rails, labeling and supplying user-specific electronic components.

| Contact: CONTA-CLIP Verbindungstechnik GmbH Christian Quade Otto-Hahn-Str. 7 33161 Hövelhof Germany tel.: +49 . 52 57 . 98 33 - 0 fax: +49 . 52 57 . 98 33 - 33 email: quade@conta-clip.de WWW: www.conta-clip.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany tel.: +49 . 30 . 53 89 65 - 0 fax: +49 . 30 . 53 89 65 - 29 email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |