Press Release

Rising up and standing tall: pump drive gets all-around makeover

Berlin – A six-pole squirrel-cage motor with 802 kW rated power and a speed of 990 min-¹ underwent a particularly extensive scope of modifications in January 2016 at German motor manufacturer Menzel Elektromotoren. A steel mill in  Wales requested this motor as a 100 % compatible replacement for a pump drive. This required an unusually large number of design adaptations and special modifications – unlike in most projects, where these are rarely all necessary at the same time.

Illustration: A precise fit: engineers at Menzel Elektromotoren's Berlin workshop implemented extensive modifications for a replacement motor commissioned by a British steel plant.

Most notably, the horizontally positioned B3 motor was converted into a vertical V1 motor. Other adaptations include the addition of a protective roof, a special type QJ328 bearing and a special motor flange with customized dimensions, which the motor will stand on once it is installed. In addition to all this, another unique feature was required: a custom-built terminal box flange for the customer's BEAMA box, mounted in a specific spot. This flange allows the customer to install and continue to use this special clamp compartment, which is unusual on motors outside the UK, in the same position as before. Moreover, the Menzel engineers turned down the shaft to the required dimensions and switched the winding to a delta connection“. The new 100% compatible motor is due to be installed in place of the old unit in February 2016.

| Illustrations: | Wales_motor | Char.s: | 1.324 |
| --- | --- | --- | --- |
| File name: | 201602014_pm_stahlwerk_wales_en | Date: | 2016-02-25 |

About Menzel Elektromotoren

Based in Berlin, Menzel Elektromotoren GmbH has been manufacturing and distributing electric motors for more than 85 years. The medium-sized company specializes in the delivery of large electric motors, including special models, within the shortest possible time. The product range comprises high and low voltage motors, DC motors, transformers, and frequency inverters. Services include motor production and short-term adaptation of stocked motors to application-specific requirements. In order to ensure fast deliveries to the customer at all times, the company maintains a very extensive inventory including more than 20,000 motors with a maximum performance of up to 15,000 kW. Qualified engineering, experienced staff, and state-of-the-art production and testing facilities help Menzel provide excellent reliability. Menzel operates subsidiaries in the UK, France, Italy, and Sweden, and cooperates with numerous partners worldwide.

| Contact: Menzel Elektromotoren GmbH Mathis Menzel Neues Ufer 19-25 10553 Berlin Germany Tel.: +49 30 / 34 99 22 - 0 Fax: +49 30 / 34 99 22 - 999 Email: info@menzel-elektromotoren.com WWW: www.menzel-elektromotoren.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 - 0 Fax: +49 30 / 53 89 65 - 29 Email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |