Press Release

CONTA-CLIP presents Webeasy: A comprehensive I/O module series for building automation

Hövelhof – For professional building automation based on Modbus RTU, the Webeasy range of compact I/O modules from CONTA-CLIP provides a comprehensive solution for connecting sensors and actuators to central control systems. Analog, digital, or analog/digital Webeasy modules are equally suitable for installation in cabinets or decentralized in the field. At the local level, the modules can be swiftly connected via the integrated WE connectors. Without any need for additional wiring, automatic contact is ensured for the power feed and serial Modbus interface.

Figure: WE-Multi I/O, one of the modules in CONTA-CLIP's Webeasy series

For decentralized applications, individual modules can be connected via standard twisted-pair cable lines. To ensure continued control of building functions in cases of maintenance or troubleshooting of a central control unit, the Webeasy modules are available with an intervention switch. Pressing the switch decouples the devices from the automated network and allows for manual output control. In addition, the modules are equipped with a built-in processor, which provides the option to implement an emergency program for malfunctions. LEDs indicate the device status and switching status of the outputs at a glance. Network node addresses can be easily configured via screwdriver-operated rotary switches on the modules. A total of 64 Webeasy modules can be connected to a single bus with a maximum cable length of 500 meters. Providing I/O solutions for every application, the versatile Webeasy series features analog/digital input modules, digital and analog/digital output modules as well as digital and analog/digital input/output modules. The series also includes Ethernet/Modbus gateways, I/O modules with Ethernet interfaces and various modules for controlling window blinds, fan coils and lighting (including  DALI bus solutions). Webeasy modules for an easy connection of the power supply and bus cable round off the range.

| Figures: | webeasy_schraeg | Char.s: | 1,891 |
| --- | --- | --- | --- |
| File name: | 201603023_pm_webeasy_io_en | Date: | 2016-03-0X |

About CONTA-CLIP

CONTA-CLIP is one of Europe’s leading manufacturers of electric terminal blocks. Based in Hövelhof, Germany, the medium-sized, family-run company has been producing electric and electronic connection systems for the process and automation industries for more than 30 years. CONTA-CLIP supplies all industry sectors, focusing on railroad industries, shipbuilding, building automation, conveyor technology, machine and plant engineering and construction, instrumentation and control technology, control panel manufacturing, transformer manufacturing, and environmental technology. The company consists of three specialized branches: CONTA-CONNECT for electric connection technology, CONTA-ELECTRONICS for electronics and CONTA-CON for PCB edge connectors. Additionally, CONTA-CLIP provides services such as customizing housings and mounting rails, labeling and supplying user-specific electronic components.

| Contact: CONTA-CLIP Verbindungstechnik GmbH Christian Quade Otto-Hahn-Str. 7 33161 Hövelhof Germany tel.: +49 . 52 57 . 98 33 - 0 fax: +49 . 52 57 . 98 33 - 33 email: quade@conta-clip.de WWW: www.conta-clip.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany tel.: +49 . 30 . 53 89 65 - 0 fax: +49 . 30 . 53 89 65 - 29 email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |