Press Release

Inductive proximity sensors for Ex zones 0/20 heat resistant up to +140 °C

Gettorf – Sensor manufacturer EGE introduces IGEXH series intrinsically safe inductive sensors for high-temperature applications in zone 0 hazardous gas atmospheres and zone 20 dust atmospheres. Designed to withstand extreme ambient temperatures from -20 °C to +140 °C, IGEXH sensors operate reliably even with frequent temperature variations. The rugged proximity switches manufactured from 1.4571 stainless steel and PEEK provide IP68/IP69K ingress protection. The companion signal processing unit, the IKM 122 Ex amplifier, is installed outside the hazardous area. At launch, the series features M12 and M18 type sensors, with more to follow at a later time. The sensors are connected via a 2 meter FEP cable.

Figure: Inductive IGEXH sensors are suitable for hazardous dust and gas atmospheres up to +140 °C

| Figures: | F1704_IGEXH_150 | Char.s: | 702 |
| --- | --- | --- | --- |
| File name: | 201604062_pm_IGEXH_en | Date: | 2016-04-22 |

About EGE

EGE-Elektronik Spezial-Sensoren GmbH has been developing and manufacturing special purpose sensors for automation applications since 1976. The company serves leading international producers from a wide range of industries. Its product portfolio includes flow controllers, infrared, opto and ultrasonic sensors, capacitive proximity switches, light barriers and inductive proximity switches. EGE also provides sensors for highly sensitive applications, e.g. hazardous areas. The development department's highly qualified staff cooperates closely with all customers, ensuring continuous product updates and enhancement. A total of 89 employees, including 20 engineers and technicians, generate gross sales of approx. 19.5 million Euros worldwide.

| Contact: EGE-Elektronik Spezial-Sensoren GmbH Sven-Eric Hiss Ravensberg 34 24214 Gettorf Germany Tel.: +49 43 46 / 41 58 -0 Fax: +49 43 46 / 56 58 Email: info@ege-elektronik.com WWW: www.ege-elektronik.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 Email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |