Press Release

An eye on hot spots in steelworks and metals processing – Endurance infrared thermometer

Fluke Process Instruments will showcase infrared temperature monitoring solutions tailored to primary and secondary metals manufacturing processes at the 2016 HeatTreatmentCongress in Cologne, Germany, in hall 4.1, at stand B-071. Geared at high-temperature applications, the new Endurance series covers wide measured temperature ranges of +550 °C to +1,800 °C and +1,000 °C to +3,200 °C, respectively. The pyrometers feature a stainless steel IP65 housing and galvanically insulated I/Os. They can be operated in one- or two-color (ratio pyrometer) mode. An optical resolution of up to 150:1 allows measurements of smaller objects from a distance.

Illustration: The rugged new infrared thermometers ensure high precision and flexible integration in all kinds of process monitoring setups

Designed for comfortable configuration and operation, the sensors feature an intuitive rear-panel user interface and a built-in web server for data archiving, traceability, and process troubleshooting. The range of sighting options has been extended to include a high-resolution on-board video camera for remote monitoring of the application and sensor alignment via Industrial Ethernet. In addition to laser sighting, which marks the position or size of the measurement spot, LED sighting projecting the actual spot size on the target is also available now. A dirty lens alarm signals when cleaning is necessary, saving time on regular maintenance. Accessories include an air-purge collar. The rugged sensors operate reliably at ambient temperatures up to +65 °C or up to +315 °C using cooling accessories. The manufacturer provides a best-in-class four-year warranty.

Fluke Process Instruments at the HeatTreatmentCongress

Koelnmesse, Cologne, Germany, 26–28 October, 2016

Hall 4.1, stand B-071

| Illustrations: | endurance_appl | Char.s: | 1,517 |
| --- | --- | --- | --- |
| File name: | 201605016_pm_endurance_hk2016_en | Date: | 2016-05-25 |

About Fluke Process Instruments

Fluke Process Instruments designs, manufactures, and markets a complete line of infrared temperature measurement and profiling solutions for industrial, maintenance, and quality control applications. Distributed worldwide under the Raytek, Ircon, and Datapaq brands, the products reflect the combined experience of over 125 years in manufacturing the world’s finest temperature measurement tools and devices.

About Fluke

Founded in 1948, Fluke Corporation is the world leader in compact, professional electronic test tools. Fluke customers are technicians, engineers, electricians, and metrologists who install, troubleshoot, and manage industrial, electrical, and electronic equipment and calibration processes.

| Contact for Europe, Middle East, Africa: Fluke Process Instruments Raytek GmbH Stephan Wilke Blankenburger Str. 135 13127 Berlin Germany Tel.: +49 . 30 . 478 008 - 412 Fax: +49 . 30 . 471 0251 Email: stephan.wilke@fluke.com WWW: www.flukeprocessinstruments.com Contact for Americas, Asia-Pacific: Fluke Process Instruments Arlene Lucas-Starrh Santa Cruz, CA, USA Tel.: 800 227 8074 (US & Canada) or +1 831 458 1110 Email: arlene.lucas-starrh@fluke.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 - 0 Fax: +49 30 / 53 89 65 - 29 e-mail: info@gii.de WWW: www.gii.de |
| --- | --- | --- |