Press Release

Compact distributor for wires up to 500 mm² and 1100 A

Hövelhof – CONTA-CLIP expand their range of screw-type distributor blocks by adding the new SVBA and the SVBKA types for energy distribution in control cabinets. Both series are suited for copper leads as well as for aluminum conductors. Featuring an extremely compact design, these units facilitate potential or power distribution without the need for additional accessories. SVBA blocks are sized for small wire cross sections of 1.5 mm² up to a massive 500 mm². They connect an incoming conductor with a large cross section with up to six conductors with smaller cross sections.

Illustration 1: SVBA screw-type distributor blocks

SVBA blocks are available in five versions for currents between 85 A and 415 A, as well as in a special 1100 A version with three terminal connections. They feature rated voltages of 1000 V AC and up to 1500 V DC. All models except for the special high-current version are easy to mount by snapping them together with a plastic connecting clip. Colored marking columns for N, PE and phase allow users to code and re-code the SVBA blocks as needed. An built-in label on the block additionally shows the connected phase. SVBA blocks with up to 380 A for the North American market are UL-certified.

In contrast, all models of the SVBKA screw-type distributor series feature just two connections and facilitate the quick and easy contacting of two conductors with cross-sections ranging from 1.5 mm² up to 240 mm² for currents up to 425 A and voltages of 1000 V. For smaller conductor cross-sections, touch safety is ensured with optional covers. SVBKA blocks provide a major advantage compared to conventional terminal blocks due to their significantly slimmer and therefore space-saving design. Both SVBA and SVBKA series blocks can be mounted by simply snapping them onto a TS35 DIN rail. They can also be fixed directly to a mounting plate via a screw flange on the side. Both series ensure IP20 ingress protection for all wire cross sections.

Illustration 2: Series SVBKA

| Figures: | SVBA-Familie5 SVBKA-Familie8 | Char.s: | 1,914 |
| --- | --- | --- | --- |
| File name: | 201711067_pm_svba_svbka_en | Date: | 11-28-2017 |

About CONTA-CLIP

CONTA-CLIP is one of Europe’s leading manufacturers of electric terminal blocks. Based in Hövelhof, Germany, the medium-sized, family-run company has been producing electric and electronic connection systems for the process and automation industries for more than 40 years. CONTA-CLIP supplies all industry sectors, focusing on railroad industries, shipbuilding, building automation, conveyor technology, machine and plant engineering and construction, instrumentation and control technology, control panel manufacturing, transformer manufacturing, and environmental technology. The company consists of three specialized branches: CONTA-CONNECT for electric connection technology, CONTA-ELECTRONICS for electronics and CONTA-CON for PCB edge connectors. Additionally, CONTA-CLIP provides services such as customizing housings and mounting rails, labeling and supplying user-specific electronic components.

| Contact: CONTA-CLIP Verbindungstechnik GmbH Christian Quade Otto-Hahn-Str. 7 33161 Hövelhof Germany tel.: +49 . 52 57 . 98 33 - 0 fax: +49 . 52 57 . 98 33 - 33 email: quade@conta-clip.de WWW: www.conta-clip.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany tel.: +49 . 30 . 53 89 65 - 0 fax: +49 . 30 . 53 89 65 - 29 email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |