Press Release

Embedded vision innovations at SPIE Photonics West

At SPIE Photonics West, Vision Components will present new products geared at vision OEMs. In addition to full-fledged embedded vision systems, these include the brand-new MIPI camera modules. These ultra-compact boards are manufactured at highly competitive costs, making them ideal for applications with a large number of cameras. OEMs have a choice of two global shutter sensors and four rolling shutter sensors with resolutions up to 8.4 MP. Higher-res MIPI cameras are upcoming. The MIPI cameras can currently be connected to more than 20 CPU boards. In addition, the German embedded vision experts will present their extended range of VC Z smart cameras based on Sony Pregius sensors. These cameras achieve outstanding frame rates, for instance 88 fps at 3.2 MP resolution. The lineup includes board cameras, stereo cameras, and enclosed, standalone models. They contain a Xilinx Zynq module, a system on chip (SoC), which comprises a dual-core ARM Cortex-A9 processor with a 2 x 866 MHz clock rate as well as an FPGA. The latest addition to the VC Z series, the VCnano3D-Z laser profiler, will also be on show. Featuring Vision Components' proprietary ambient light suppression technology, this intelligent 3D vision system enables measurements under up to 100,000 lux. The onboard FPGA is pre-programmed to calculate the 3D point cloud. The ARM processor can thereby be freely programmed for further application-specific tasks such as analyzing the grayscale image.

Vision Components at SPIE Photonics West

San Francisco, 5 – 7 Feb 2019

Hall North, Booth 2621

Illustration: Vision Components presents embedded vision systems with new, powerful image sensors and a 3D laser profiler that can also analyze the grayscale image

| Illustrations: | vc_z_embedded_systems | Char.s: | 1473 |
| --- | --- | --- | --- |
| File name: | 201901015_pm_spie_photonics_west_en | Date: | 01-31-2019 |

About Vision Components

Founded in 1996 by Michael Engel, inventor of the first intelligent camera for industrial applications, Vision Components GmbH is a leading supplier in the field of machine vision. Branches and distributors represent the Ettlingen-based company throughout the world in more than 25 countries. Vision Components develops and distributes intelligent, network-compatible real-time Smart Cameras that are able to operate without a PC. These embedded vision solutions can be easily integrated into almost any machine or plant. Customers can choose between models with ARM processors and VC Linux firmware, or DSP-based models with the proprietary VCRT operating system. The product portfolio includes Smart Cameras with or without a protective housing, single board cameras, and vision sensors. Vision Components also develops custom-tailored machine vision solutions for a wide range of applications – including, amongst others, tasks in quality inspection and automation. Furthermore, VC provides software libraries for many applications such as motion capture, decoding, measurement, and positioning.

| Contact: Vision Components GmbH Miriam Schreiber Ottostr. 2 76275 Ettlingen Germany |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 5389 650 Email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |
| Tel.: +49 7243 / 216 716 Email: miriam.schreiber@vision-components.com WWW: www.vision-components.com |