Press Release

New RAFI signal indicator in elegant design for display of three status conditions

RAFI has expanded its RAFIX 30 FS+ control and signaling unit program with an ultra-flat (3.45 mm) LED signal indicator featuring a stainless steel front ring. Thanks to an integrated red and green LED, the indicator can signal three status conditions. The translucent bezel is a neutral white in standby mode, green indicates regular operating condition, and red signals faults. The signal indicator features separate terminals with reverse-polarity protection for 2.8 mm x 0.8 mm quick connectors and operating voltages of 8 VDC to 30 VDC. The new signal lamps feature IP65 degree of protection to the front side and, like all RAFIX 30 FS+ control and signaling units, they fit standard 30.3 mm installation openings. With a collar diameter of 34.5 mm and a mounting depth of 31.85 mm, the integrated lamps are suitable for a minimum grid spacing of 35 mm.

Caption: RAFIX 30 FS+ signal indicator in three status conditions

| Image/s: | RAFIX_30_FS-Meldeleuchten_EN | Characters: | 858 |
| --- | --- | --- | --- |
| File name: | 202005025_PM_RAFIX_30_FS-Meldeleuchten_mit_rot-gruen-LED_en | Date: | 07-01-2020 |

About the RAFI group

Founded in 1900, RAFI today develops and produces electromechanical components and systems for human-machine interaction. The range of products includes pushbuttons, switches, touchscreens, control systems and electronic assemblies. RAFI products are employed in many industries including automation, medical technology, machine and plant engineering, road and railway vehicles, household appliances and telecommunication. The RAFI group operates internationally with more than 2,000 employees at sites in Germany, Europe, China, and the USA. Its headquarters are in Berg, Germany.

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Str. 128-134 88276 Berg, Germany Phone: +49 751 89-1307 Fax: +49 751 89-1300 Email: artur.krug@rafi.de Internet: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin, Germany Phone: +49 30 53 89 65-0 Fax: +49 30 53 89 65-29 Email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |