Press Release

Smart drive assumes local control

Enabling centralized as well as autonomous operation

Bargteheide – Frequency inverters from NORD DRIVESYSTEMS can react flexibly in case of disrupted communication with a central control system. The on-board, pre-programmed PLC can take control, initiate a defined state for halting operations, or keep the application running. In process plants this can help avoid costs, for instance by preventing spoiled batches. In manufacturing facilities, material flow can be maintained. As NORD intelligent drives feature various interfaces and are able to evaluate sensor and actuator data, optimal integration in the application is ensured. Autonomous control capability obviously has other uses beyond fallback scenarios. In some instances, users may wish to deliberately switch the smart drive over to local control. For set-up, testing, or maintenance, the distributed frequency inverter can additionally be equipped with switches for manual drive direction and speed control. The integrated PLC functions are programmed using IEC 61131-3 "Structured Text" or "Instruction List" text-based languages. For straightforward, user-friendly application development, NORD CON software is provided without any charge or license fees.

Illustration: In case of an intentional or accidental disconnection of the central control system, the inverter PLC can execute pre-programmed procedures to keep the application running or bring it to a defined standstill

| Illustrations: | plc_appl_interrupt | Char.s: | 1,156 |
| --- | --- | --- | --- |
| File name: | 201604042_pm_hybrid_control_capability_en | Date: | 2016-09-12 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 540 mn in the 2015 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide/Hamburg Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |