Press Release

Industrial gear units with 190 kNm output torque

Even more comprehensive UNICASE gear unit portfolio

Bargteheide – NORD DRIVESYSTEMS extends the successful industrial gear unit range by adding a new size with 190 kNm output torque. The series now comprises nine sizes and covers torques from 25 kNm to 250 kNm. The addition of the new size 14 units allows for configurations tailored even more precisely to individual applications. Featuring a single-piece UNICASE housing as is standard for all NORD gear units, they achieve a longer bearing life than gear casings manufactured from jointed parts and ensure efficient power transmission and high tolerance for load peaks and jolts. They can be assembled as two or three-stage helical inline or helical bevel gearboxes with nominal transmission ratios from 7.1:1 to 400:1, or even up to 30,000:1 with an auxiliary primary stage. The input and output direction can be freely selected. NORD industrial gear units can be mounted on any of the six sides. The manufacturer configures industrial geared motors for a diverse range of uses from steel works to process plants. Application-specific features and options include reinforced bearings and shafts, extra-large bearing distance, extended output shafts, and Drywell designs with an additional oil drip disc and a leakage oil display or oil sensor. Disc and drum brakes, dual-gear setups, auxiliary motors, IEC motor adapters, turbo couplings, axial fans, motor swing bases, torque limiting backstops, and cooling and heating systems are available as well.

Illustration: A new size in the NORD industrial gear unit range provides the proven advantages: high load capacity, application-specific configuration, and flexible installation

| Illustrations: | industriegetriebe_bg_14 | Char.s: | 1,440 |
| --- | --- | --- | --- |
| File name: | 201604058_pm_igu_size_14_en | Date: | 2016-04-26 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,200 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 540 mn in the 2015 business year. Subsidiaries in 36 countries around the world and an extensive distribution and service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide/Hamburg Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |