Press Release

Record-size industrial gear unit in a one-piece housing

NORD DRIVESYSTEMS, a leader in drive technology, has engineered an industrial gear unit with 240,000 Nm rated torque load and various application-specific features for a phosphate mine in Morocco. It is to date the largest system with a one-piece gear case.

Illustration: Tailored to specific applications, the conveyor drive with an industrial gear unit in a one-piece housing ensures high load-bearing capacity and ultra-reliable performance. (The brake guard and gear inlet have been removed for the purpose of this photo.)

The drive unit comprises an SK 15407 industrial bevel gear unit, a medium-voltage electric motor with a 450 kW performance rating, a swing base, a hydraulic coupling, and an electro-hydraulic brake. It is one of 26 systems NORD designed according to an extremely stringent set of specifications and taking into account the harsh environmental and operating conditions. These units drive a conveyor that is over two kilometers long and carries phosphate ore with loads exceeding several hundred tons. The high-performance gear unit meets the client’s demanding requirements, in particular maximum uptime and high tolerance to peak loads and impacts. The UNICASE gear design prevents leaks and delivers excellent radial and axial load capacities with a small footprint. The industrial gear design unit allows for mounting on all six sides as well as by means of a flange. NORD’s Casablanca office engineered the drive with the assistance of NORD engineers in France and Germany. The components at the inlet of the gear unit are covered by safety guards to protect operators from the rotating parts. The application side, which includes the gear unit, can be fully disconnected from the motor side via the hydraulic coupling. The solution ensures ultra-reliable operation and a high level of safety.

| Illustrations: | 1403b_igu_morocco | Char.s: | 1,553 |
| --- | --- | --- | --- |
| File name: | 201610004_pm_igu_morocco_en | Date: | 2016-12-06 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 540 mn in the 2015 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide/Hamburg Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |