Press Release

Versatile plug&play drives for conveying tasks

NORD DRIVESYSTEMS presents the newly developed NORDAC LINK series field distribution systems. Coded plug-in connectors for power, communications, sensors, and actuators enable fast, safe installation and commissioning of these new AC vector drives and motor starters. LEDs that indicate switching states, operation modes, and signal states allow operators to diagnose errors directly on site. Maintenance and control switches on the devices facilitate plant servicing and system set-up. Designed for flexible configuration, NORDAC LINK drives are especially suitable for conveying applications, but can also be used with other machines and systems. Integrated functionality ranges from rotary encoder support and brake management to PI control and sequence control through an integrated PLC. The drives feature a high overload capacity. They enable very precise control of either asynchronous or synchronous motors and reliably deliver full torque even at zero speed. Moreover, the field distribution systems provide extensive monitoring functions to protect the mains, the motor, and the driven machine. Power supply can be daisy-chained from one drive to the next. This greatly reduces the cabling effort and costs, particularly in complex applications with hundreds of drive axes.

Illustration: Featuring plug-in connections and numerous interfaces, the field distribution systems enable flexible plant designs and quick installation

| Illustrations: | nordac_link_size1_gm | Char.s: | 1,283 |
| --- | --- | --- | --- |
| File name: | 201610042_pm_nordac_link_en_logimat | Date: | 2017-02-27 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 mn in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide/Hamburg Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |