Press Release

Industrial gear units with extruder flanges

As an all-new supplement to the modular industrial gear range, NORD DRIVESYSTEMS now provides extruder flanges optimized for heavy duty operation. Several different extrusion flanges are available for each of the industrial gear units from size 5 to size 11, with rated torques from 15 kNm to 80 kNm. Almost all usual dimensions can thus be adapted. Extra-large thrust bearings ensure that all process forces are absorbed and provide enhanced durability for long lifespans. This new option for the industrial gears enables primary and secondary plastics and rubber manufacturers and their suppliers to create safe and highly reliable drives in very customizable configurations. The NORD industrial gear range offers a variety of input and output shafts and gaskets, flexible mounting directions, and thermal monitoring solutions. The extruder flange as well as industrial gear units in two additional sizes will be showcased for the first time at the 2017 Hannover Messe exhibition.

NORD DRIVESYSTEMS at Hannover Messe, Hanover, Germany

24 – 28 April 2017

Hall 15, Stand H31

Illustration: NORD now supplies robust extruder drives complete with flanges in various sizes

| Illustrations: | igu_extruder_flange | Char.s: | 982 |
| --- | --- | --- | --- |
| File name: | 201704004_pm_igu_extruder_en | Date: | 2017-04-13 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 mn in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |