Press Release

More powerful conveyor drives forthcoming

In September 2017, the recently introduced NORDAC LINK series of field distribution systems will be further supplemented by frequency inverters for motors rated up to 7.5 kW. With these additions, the new series from NORD DRIVESYSTEMS will then comprise a comprehensive line-up of drive solutions specifically tailored to networked conveyor systems with many drive axes. The new size 2 systems will be deployed wherever smaller drives do not suffice and extra power is needed – for instance, in inclined conveyors, hoists, or long belt conveyors.

Illustration 1: Distributed drive technology from NORD DRIVESYSTEMS: the new systems take over heavier-load horizontal and vertical conveying tasks

Hoist functions and the STO and SS1 safety functions according to EN 61800-5-2 are included by default. By integrating geared motors that are produced in-house into the drive system configuration, NORD is able to supply complete solutions from a single source to system engineers and operators of warehousing, distribution center, intralogistics, or baggage handling facilities. Interfaces for all common fieldbuses and Industrial Ethernet protocols are supported. Plug connectors for power, sensors, and communication lines ensure particularly fast and error-free installation and maintenance. The size 2 frequency inverters complement the smaller drive size and motor starters launched earlier in 2017, which cover a large part of all intralogistics drive applications in the 0.55 to 3 kW range.

A video clip (http://nord.click/vq7g) shows the extensive functional features of the NORDAC LINK series, the comfortable and flexible control options, and the especially easy commissioning of these field distribution systems.

Illustration 2: A clip on the NORD YouTube channel about the NORDAC LINK series of field distribution systems demonstrates key features such as the simple and flexible connection options

| Illustrations: | test_center_nordac_link_size2 nordac_link_fds_film_2017_A | Char.s: | 1,568 |
| --- | --- | --- | --- |
| File name: | 201704035_pm_nordac_link_size2_en | Date: | 2017-04-11 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 mn in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |