Press Release

Modular industrial gear units in additional sizes

NORD DRIVESYSTEMS introduces two new gearboxes for nominal torques of 15 and 20 kNm. With these latest additions to the line-up, the series now comprises 11 gearbox sizes that deliver output torques up to 250 kNm. The NORD industrial gear series offers a particularly great variety of configuration options for application-specific drive solutions. The modular NORD product range includes dual-gear setups, auxiliary drives, brakes, torque arms, backstops, swing bases, and – as the latest special feature – extruder flanges. In addition, there are a variety of sealing options and solutions for monitoring and temperature management. The gear units can be mounted on all six sides. Gear ratios can be configured in fine increments from 5.54 : 1 to over 30,000 : 1 – with two, three, or four gear stages, and with an auxiliary primary gear stage if so required. All NORD industrial gear units feature a single-piece UNICASE housing. This ensures excellent longevity, a very high power density, compact dimensions, and high overload capacities. Combining industrial gear units with motors and drive electronics, NORD configures complete drive systems for heavy-duty operation in conveying systems, pumps, and agitators. Designated major application fields for these units include bulk handling, the cement industry, steel industry, process engineering, woodworking, sugar processing, and wastewater management.

Illustration: The new industrial gear units greatly increase the possibilities for configuring application-specific drives in the load range up to 20,000 Nm, for example with a dual gear setup and swing base

| Illustrations: | igu_size_5-6 | Char.s: | 1,409 |
| --- | --- | --- | --- |
| File name: | 201704042_pm_igu_size_5-6_en | Date: | 05-24-2017 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,300 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 mn in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |