Press Release

More than redundant: Special encoder with three separate measuring systems

Berlin – Sensor specialist FSG presents the new special magnetic encoder series MH680-III-MU-G which provides maximum reliability through multiple redundancy. The single-turn encoder is equipped with three electrically isolated Hall measuring systems to meet even the most demanding requirements in safety-related applications, i.e. in cases where redundant signals for monitoring do not suffice or additional signal outputs are needed to visualize the process.

Illustration: The special encoder from FSG features multiple redundancy for safety-relevant applications with maximum reliability requirements.

The device enclosures are manufactured from Hart-Coat aluminium and provide corrosion, shock and vibration resistance. Thanks to their wide temperature range of -30 °C to +80 °C and IP67 ingress protection they are suitable for even the most demanding environments. The new encoder features a resolution of 14 bit and covers a measuring range of 0-360°. Signal output is provided per channel via a 4-20 mA current interface.  FSG provides each channel with its own membrane keypad for signal setting, therefore allowing for independent calibration of every signal output.

| Figures: | MH680-III-MU-G | Char.s: | 1,023 |
| --- | --- | --- | --- |
| File name: | 201704045_pm_spezialdrehgeber_mh680_en | Date: | 2017-04-18 |

About FSG

FSG Fernsteuergeräte, a leading supplier of measuring and sensor technology, was founded in 1946. The company develops and manufactures high-quality measuring sensors for automation and safety engineering applications, providing a 90 % depth of production. The product portfolio includes a wide range of customer-oriented systems solutions: linear displacement transmitters, angular position transducers, wind warning systems, manual X/Y control transmitters, pedal actuated transmitters and signal indication components. FSG employs a staff of 400 at its Berlin headquarters and in its Kablow and Heppenheim plants, about 30 % of whom work in research and development, sales and quality management.

| Contact: FSG Fernsteuergeraete Jahnstr. 68+70 12347 Berlin Germany Tel.: +49 30 / 6 2 91 1 Fax: +49 30 / 62 91 277 Email: info@fernsteuergeraete.de WWW: www.fernsteuergeraete.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65-0 Fax: +49 30 / 53 89 65-29 e-mail: info@gii.de WWW: www.gii.de |
| --- | --- | --- |