Press Release

In confined spaces, IKAL series LVDT sensors precisely measure extremely short distances

Ottobrunn – In very close quarters, Inelta Sensorsysteme's extremely slender LVDT displacement sensors (linear variable differential transformers) of the IKAL series ensure highly accurate position detection and path length measurements. With a housing diameter of only 8 mm and a housing length of no more than 96 mm even for the longest version, these sensors fit into the most tightly confined installation spaces. They are available in four different versions for measuring distances up to 2 mm, 5 mm, 10 mm and 20 mm.

Illustration: Inelta's IKAL series miniature LVDTs are merely 8 mm wide and weigh only 30 g.

The sensors achieve a standard linearity tolerance of <0.5% and are optionally available with a linearity tolerance of <0.25% for even more demanding applications. Thanks to their non-contact inductive measuring principle, these LVDT sensors are wear-free. The miniature displacement sensors are made from nickel-plated steel and provide IP65 ingress protection. They are long-lived and extremely rugged – they are not only designed for environmental temperatures from -25 °C to +85 °C, but also withstand shock impact and vibrations of 200 g over 2 ms or 10 g over sine wave frequencies from 2 Hz to 2000 kHz, making them exceptionally resistant even to severe mechanical stress. IKAL series sensors are therefore suitable for very diverse applications, ranging from medical technology to machine building, to the agricultural sector, ships, test facilities, or special purpose machine engineering. Standard supply for all models includes a one meter cable. Other lengths are available on request. To complement IKAL series displacement sensors, Inelta also offers compatible external IMA2 LVDT sensor signal amplifiers for 0 .. 5 V, 0..10 V, ±5 V, ±10 V, or 0/4..20 mA output. The IVM2 LVDT print module with a 0 .. 10V signal output is also available to facilitate an integration into custom electronics. In addition, Inelta provides customer-specific sensor types on request for options such as individual calibrations, special cable lengths, or an extended temperature range.

| Figures: | IKAL | Char.s: | 2,047 |
| --- | --- | --- | --- |
| File name: | 201705015_pm_ikal_en | Date: | 08-02-2017 |

About Inelta

Headquartered in Ottobrunn near Munich, inelta Sensorsysteme GmbH & Co. KG is part of the inelta group, which also comprises PIL Sensoren GmbH based in Erlensee near Frankfurt/Main, and VYPRO s.r.o., a production company in Trenčín, Slovakia. inelta Sensorsysteme draws on approxamately 20 years of experience in sensor development, production, and distribution. The product range includes sensors for distance and dimension measurement, force sensors, sensor signal amplifiers and actuator-sensor systems. PIL has been developing, manufacturing, and distributing ultrasonic sensors for ca. 30 years and VYPRO is focused on sensor processing, confection of cables and connectors. The company group is particularly focused on industry-specific and customer-specific sensor solutions, and continues to apply a wealth of interdisciplinary know-how to expand the scope of such offerings.

| Contact: inelta Sensorsysteme GmbH & Co. KG Katrin Seubert Haidgraben 9a D-85521 Ottobrunn Germany Tel.: 0 89 / 45 22 45-0 Fax: 0 89 / 45 22 45-744 Email: katrin.seubert@inelta.de WWW: www.inelta.de |  | gii die Presse-Agentur GmbH Immanuelkirchstraße 12 10405 Berlin Germany Tel.: 0 30 / 53 89 65-0 Fax: 0 30 / 53 89 65-29 Email: info@gii.de WWW: www.gii.de |
| --- | --- | --- |