Press Release

New Tilted Diamond+ signal lamp series

Berg/Ravensburg – The signal lamps from the new Tilted Diamond+ series developed by RAFI together with renowned product designer Luigi Colani are characterized by special brightness, impact resistance, low maintenance properties, and an exceptional lens design. The name Tilted Diamond refers to the diamond-shaped lenses in the bezel which create a unique scattered light effect.

Image: Low consumption, modern design, comprehensive range of accessories: The new Tilted Diamond+ signal lamp series with LED lighting

RAFI purposefully optimized the light refraction of the lenses to achieve perfect illumination. The consistently high visibility across 360 degrees makes the lamp easy to see, even at long distances. Four extremely bright LEDs with a power consumption of only 0.63 W are located inside the lamps. The lamps are available in yellow, green, blue, and transparent/white and are maintenance-free for up to 50,000 hours. A reliable two-screw mount that can be secured from inside or outside the housing ensures rapid assembly. For connection to a 24 V AC/DC power supply, the Tilted Diamond+ signal lamps can be supplied with CAGE CLAMP® clamped connections for direct wiring or with 4-pin M12 plugs. The signal lamps with an installation height of 70.1 mm (CAGE CLAMP®) or 83.55 mm (M12) are designed for a temperature range of between -30 °C and +60 °C and exhibit a IP65 and IP67 degree of protection on the front side. The range of accessories includes powder coated support tubes which are available in 100 mm, 250 mm, and 400 mm sizes as well as a support tube in a 90° angled and 100/100 mm version.

| Figures: | tilted_diamond_titel | Characters: | 1,634 |
| --- | --- | --- | --- |
| File name: | 201609043_pm_tilted_diamond+ | Date: | 05-12-2017 |

RAFI Group company background

Founded in 1900 under the name “Elektrotechnisches Institut”, RAFI now develops and produces electromechanical components such as pushbuttons and switches, operating systems such as touch screens, keyboards, electronic components, and systems for man-machine communication. RAFI products are used in more than 30 industries, e.g., electrical medicine, mechanical engineering, road and railway vehicles, household appliances, and telecommunications. The RAFI group operates internationally with approx. 2,000 employees at ten sites in Germany, Europe, China, and the USA. The RAFI Group headquarters are located in Berg, close to Ravensburg, in Baden-Württemberg, Germany.

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Straße 128-134 88276 Berg Tel.: +49 (0)751 89-1307 Fax: +49 (0)751 89-1300 E-mail: artur.krug@rafi.de Internet: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstraße 12 10405 Berlin Tel.: +49 (0)30 53 89 65-0 Fax: +49 (0)30 53 89 65-29 E-mail: info@gii.de Internet: www.gii.de |
| --- | --- | --- |