Press Release

Predictive maintenance and optimal use of resources

NORD DRIVESYSTEMS is developing cost-efficient and reliable virtual sensor functions for condition monitoring. The meaning of virtual sensors is explained using the oil lifespan as an example. This is to empower drive technology to schedule maintenance dates solely based on calculations, with no expense for hardware sensors. The onboard PLC evaluates extensive operational datasets on current, voltage, and speed. From this data available in the inverter, the drive is always able to indirectly infer the current oil temperature. Taking product-specific characteristics of the lubricant into account, oil aging can be determined, allowing for optimal utilization of the lubricant. NORD has validated through testing that the calculated oil temperature curve is nearly congruent with the real, measured temperature curve. Working up to launch a fully operational solution soon, NORD is currently validating temperature curves under various load conditions. Predictive maintenance functions are expected to be commercially available in all NORD drive electronics units with an onboard PLC from late 2018.

Illustration: In applications with steady long-term load profiles, the drive PLC determines the best oil change interval without costly sensors

AT A GLANCE: Virtual sensors for predictive maintenance

•	Function in frequency inverters with an integrated PLC

•	Precise definition of maintenance intervals helps
- reduce operating costs
- increase plant availability

•	Due for launch: late 2018

•	Pure software solution without hardware costs for sensors/control units

| Illustrations: | process_data_pump_drive | Char.s: | 1,104 |
| --- | --- | --- | --- |
| File name: | 201706038_pm_predictive_maintenance_en | Date: | 11-23-2017 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,600 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 million in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |