Press Release

Highly efficient and hygienic: IE4 smooth-surface motors

NORD DRIVESYSTEMS has expanded its range of high-efficiency smooth-surface motors. The new permanent-magnet synchronous motors without cooling fins achieve level IE4 / super premium efficiency. This can greatly benefit the food, beverage, and pharmaceutical industries, and other hygienically demanding applications. The efficient smooth-surface motors are suitable for use in dry areas as well as in applications requiring frequent cleaning. As they generate very little excess heat, they need no fans and therefore do not contribute to the spreading of germs. The IE4 or Super Premium Efficiency synchronous motors operate significantly more efficiently than induction motors, specifically in the partial load range. This results in substantially lower cost for energy consumption and lower TCO. The motors furthermore feature a particularly high power density and a very long product life. Frequency inverters can be mounted directly onto the motor or near the motor for perfect flexibility.

Illustration: NORD IE4 smooth-surface motors meet the highest standards of efficiency, reliability, and durability under adverse conditions

Three motor sizes (80, 90, 100) with power ratings from 0.75 to 2.2 kW are available. They complement the existing smooth-surface induction motor range, which already covers outputs from 0.37 to 1.1 kW. The motors can be supplied with a brake. For washdown-enabled inverter-controlled drive systems with an IP66/IP69K protection rating, NORD can draw on four different suitable gearbox series. Washdown drive configurations all feature die-cast aluminum housings with smooth surfaces, designed so that cleaning fluids and foams easily run off. For extra corrosion protection, they can be fitted with the nsd tupH Sealed Surface Conversion System, which is approved for food and drink applications in accordance with FDA Title 21 CFR 175.300.

AT A GLANCE:

IE4 / Super Premium Efficiency smooth-surface motors

•	High-efficiency permanent-magnet synchronous motors

•	Motor size: 80, 90, 100

•	Rated output: 0.75 kW, 1.1 kW, 2.2 kW

•	Suitable for washdown

•	Ingress protection IP66, optional IP66/IP69K

| Illustrations: | nsd_tuph_group | Char.s: | 1.735 |
| --- | --- | --- | --- |
| File name: | 201707037_pm_ie4_smooth-surface_motors_en | Date: | 08-02-2017 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,500 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 million in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |