Press Release

New, highly flexible drive electronics and robust gearboxes in additional sizes

NORD DRIVESYSTEMS puts on two consecutive showcases in Shanghai this coming November. At CeMAT Asia and at CIIF IAS, the German drive expert will present various new developments, chief among them NORDAC LINK field distribution systems, which have been designed for easy installation, commissioning, operation, and servicing in conveyor applications. The manufacturer supplies these user-friendly new frequency inverters and motor starters configured to customer requirements. All sensor, communications, and supply lines can be easily connected via coded plugs. Maintenance switches, key switches, and direction switches ensure direct user access to every single axis. Notably, NORD offers drive configurations with a reduced number of variants for large plants. Such standardization has considerable cost saving potential in terms of purchase, installation, stock-keeping, and maintenance expenses.

Illustration: The new VFD with plug & play connectors enables very speedy, comfortable installation and easy maintenance

Available for motor sizes up to 160 kW, all NORD VFDs are IIoT and Industry 4.0 ready. Featuring PI controllers and an integrated PLC, they can carry out logical sequences and take care of process control on their own. The built-in PLC can monitor the drive system, evaluate sensor data, and independently assess the state of the unit. A fully operational solution for predictive maintenance based on PLC data analysis is currently in development at NORD and will soon be commercially available. This will enable service intervals to be extended and improve overall system availability.

Not least among NORD’s new products, MAXXDRIVETM industrial geared units will be showcased with their outstanding variety of configuration options. The series has recently been expanded by two new sizes for nominal torques of 15 and 20 kNm. It now comprises 11 gearbox sizes with output torques up to 250 kNm. The modular MAXXDRIVETM range includes dual-gear setups, auxiliary drives, brakes, torque arms, backstops, swing bases, and extruder flanges. All NORD industrial gear units feature a single-piece UNICASE housing. This ensures excellent longevity, compact dimensions, a very high power density, and high overload capacities. Combining industrial gear units with motors and drive electronics, NORD configures complete drive systems for heavy-duty operation.

NORD DRIVESYSTEMS will be at

CeMAT (31 Oct. – 3 Nov. 2017, Shanghai New International Expo Center)

Hall W3, Booth B3-1

and

CIIF IAS (7 – 11 Nov. 2017, National Exhibition and Convention Center, Shanghai)

Hall 5.1, Booth B061

| Illustrations: | nordac_link_size1_gm | Char.s: | 2,251 |
| --- | --- | --- | --- |
| File name: | 201708045_pm_cemat_ciif_ias_china_en | Date: | 09-08-2017 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,600 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 million in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |