Press Release

Efficient drive solutions with a small line-up of variants

Specifically designed for intralogistics and baggage handling systems, the new LogiDrive standardized AC vector drives from NORD DRIVESYSTEMS facilitate planning, configuration, and spare part management through a project-based reduction of variant complexity. These drives meet the highest efficiency standards – IES2 system efficiency and IE4 or Super Premium Efficiency for the motor by itself – and reach excellent efficiencies even in the partial load range and at low speeds. They therefore pay for their initial cost within a few years or even only months. Total expenses over the product lifespan are significantly reduced. The systems allow for simple daisy-chaining; short power lines can be connected from one drive to the next.

Illustration: Designed for intralogistics and baggage handling systems, LogiDrive units save operating expenses as well as costs for stocking spare parts

The user-friendly systems consist of a helical-bevel gearbox, an IE4 permanent magnet synchronous motor, and a frequency inverter for installation near the motor. They are easy and quick to install thanks to all pluggable connectors. Maintenance switches, key switches, and direction switches on the device allow for flexible direct access to individual drive axes for set-up or service. Built into a light alloy case, the compact drives are also easy to handle. Boasting a large overload capacity, the drives come in three preferred sizes that match the typical performance requirements in intralogistics and airport applications. Conveyor speeds and running directions are regulated by the LogiDrives' frequency inverters. These VFDs are optionally available with an incremental encoder for highly dynamic applications. The STO and SS1 safety functions according to EN 61800-5-2 are included by default. Drive-related sensors can be connected via M12 plugs. Sensor data collected by the inverters can be passed on to higher-level systems, which reduces otherwise necessary wiring. LogiDrive installations can be deployed around the world thanks to comprehensive certifications. Interfaces for all common bus systems are readily available.

AT A GLANCE: LogiDrive

•	Variant reduction minimizes procurement, commissioning, and maintenance costs

•	High energy saving potential

•	Easy to operate, low maintenance

•	Optimized for postal hubs, intra-logistics, airport baggage handling

| Illustrations: | nordac_link_size1_gm | Char.s: | 1,979 |
| --- | --- | --- | --- |
| File name: | 201710060_pm_logidrive_ie4_en | Date: | 11-28-2017 |

About NORD DRIVESYSTEMS

A developer and manufacturer of drive technology for over 50 years, NORD DRIVESYSTEMS employs more than 3,600 people and is one of the world's leading suppliers of full-scale, comprehensive drive solutions. NORD's portfolio ranges from standard drives to customized solutions for demanding application requirements, e.g. based on energy-efficient or explosion-protected drives. Gross sales amounted to EUR 560 mn in the 2016 business year. Subsidiaries and distributors in 89 countries around the world and an extensive service network ensure minimal lead times and provide customer-oriented services wherever needed on short notice. NORD’s wide variety of gear types covers torques from 10 Nm to 250 kNm and more. The company also supplies motors with outputs from .12 kW to 1,000 kW and manufactures frequency inverters up to 160 kW. NORD's inverter line-up features conventional models for installation in control cabinets as well as design types for fully integrated drive units in decentralized automation environments.

| Contact: Getriebebau NORD GmbH & Co. KG Member of the NORD DRIVESYSTEMS Group Getriebebau-Nord-Str. 1 22941 Bargteheide Germany Tel.: +49 45 32 / 2 89 -0 Fax: +49 45 32 / 2 89 -22 53 email: info@nord.com Internet: www.nord.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 30 / 53 89 65 -0 Fax: +49 30 / 53 89 65 -29 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |