Press Release

RAFI E-BOX now with M12 connector

RAFI's E-BOX, a particularly slim housing for one or two RAFIX 22 FS+ control devices, is now also available as a pre-configured unit with an M12 connector. No wiring is required for this ready-to-use solution that provides emergency stop buttons or simple ON/OFF switching functions at remote locations. E-BOX features a very compact size of merely 109 x 40 x 27 mm and is suitable for mounting on 40-mm profile rails or, for instance, on protective barriers. A single screw fixes the mounting clip in the profile rail groove. Users can then simply attach the E-BOX housing – it clicks and sticks.

Illustration: RAFI now offers complete, pre-configured E-BOX control units with M12 connectors

E-BOX M12 is available as a 4-pole or 8-pole version with illuminated pushbuttons. The pre-configured range currently comprises models with an emergency stop or a pushbutton, or both, or with two pushbuttons (1 NC, 1 NO). The housing tops for the emergency-stop versions are colored signal yellow, the pushbutton ones are gray. Different pushbutton designs are available for various uses: ON/OFF switches with red and green blinds (optionally flat or raised), gray pushbuttons with arrows for lifting and lowering movements. Users can individually mark the button of the single-pushbutton E-BOX model with RAFI's FLEXLAB labeling system. The new E-BOX M12 housings feature IP65 ingress protection and a -25 °C to +70 °C ambient temperature range.

| Illustrations: | e-box_m12_gruppe | Char.s: | 1,344 |
| --- | --- | --- | --- |
| File name: | 201803009_pm_e-box_m12_en | Date: | 05-08-2018 |

Company background RAFI group

Founded in 1900, RAFI now develops and produces electromechanical components such as pushbuttons and switches, operating systems such as touch screens, keyboards, electronic components, and systems for man-machine communication. RAFI products are employed in more than 30 industries, e.g., in medical equipment, mechanical engineering, road and railway vehicles, household appliances, and telecommunications. The RAFI group operates internationally with approx. 2,100 employees at ten sites in Germany, Europe, China, and the USA. The group’s headquarters are located in Berg (Baden-Württemberg, Germany).

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Str. 128-134 88276 Berg Germany Tel.: +49 . 751 . 891 307 Fax: +49 . 751 . 891 300 e-mail: artur.krug@rafi.de WWW: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Tel.: +49 . 30 . 5389 650 Fax: +49 . 30 . 5389 6529 email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |