Press Release

New RAFI red/green signal indicator

RAFI has expanded its RAFIX 22 FS+ control component program with a signal indicator featuring an integrated red and green LED. The indicator can display three status conditions in one light. The translucent bezel is a neutral white in standby mode, green indicates regular operating condition, and red signals faults. The indicators have a diameter of 29.8 mm and an installation height of 14.4 mm. The domed surface makes the indicators easily visible also from the side. Like all RAFIX 22 FS+ control and signaling units, they fit standard 22.3 mm installation openings and feature IP65 degree of protection to the front side. The mounting depth is 25.25 mm. The display of different status conditions is possible due to separate terminals with reverse-polarity protection for 2.8 mm x 0.8 mm quick connectors and operating voltages of 8 VDC to 30 VDC.

Caption: RAFIX 22 FS+ signal indicator in three status conditions

| Image/s: | RAFIX_22_FS-Meldeleuchten_EN | Characters: | 855 |
| --- | --- | --- | --- |
| File name: | 202005028_PM_RAFIX_22_FS-Meldeleuchten_mit_rot-gruen-LED_en | Date: | 07-21-2020 |

About the RAFI group

Founded in 1900, RAFI today develops and produces electromechanical components and systems for human-machine interaction. The range of products includes pushbuttons, switches, touchscreens, control systems and electronic assemblies. RAFI products are employed in many industries including automation, medical technology, machine and plant engineering, road and railway vehicles, household appliances and telecommunication. The RAFI group operates internationally with more than 2,000 employees at sites in Germany, Europe, China, and the USA. Its headquarters are in Berg, Germany.

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Str. 128-134 88276 Berg, Germany Phone: +49 751 89-1307 Fax: +49 751 89-1300 Email: artur.krug@rafi.de Internet: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin, Germany Phone: +49 30 53 89 65-0 Fax: +49 30 53 89 65-29 Email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |