Press Release

Customized OEM joysticks from RAFI for all control requirements

With its JOYSCAPE joystick platform and extensive add-on options, RAFI is able to implement custom control solutions for any application purpose and with optimum ergonomics for the job. Four differently dimensioned platform modules cover all use cases in various industries such as mechanical engineering, medical technology or construction and agricultural machinery. For heavy-duty applications, RAFI uses its JOYSCAPE ROUGH model with a shock resistance of 110 Nm. Ergonomic multifunction joysticks developed in close cooperation with the customer ensure easy and intuitive operation even under the toughest conditions.

Photo: The new multifunction joystick from RAFI for VALTRA tractors developed from the basic JOYSCAPE ROUGH model.

For challenging but less rugged applications, the joystick platform offers the versatile JOYSCAPE MULTI basic model. This version is also available with customized handles. Depending on requirements, the manufacturer can install thumb joysticks, rockers, pushbuttons and other actuator or signal elements. Where installation space is tight and control tricky, JOYSCAPE BASIC with free tilt function in the x/y plane is the optimal solution. The smallest model in the range is the compact thumb joystick JOYSCAPE TINY. It is designed for flexible integration into joystick handles or other control elements. All variants use wear-free 3D Hall sensors for motion detection. They have an operating life of up to five million actuation cycles. For high safety requirements, the sensor system is also available in a redundant design. The ferromagnetic steel housing effectively shields the sensor system, providing additional ruggedness. The joysticks are fully manufactured in-house and configured with various rockers, angles of deflection, operating forces or control components. This is how RAFI ensures seamless integration of its products into diverse customer systems. Optional extras are also available such as illuminated handles for work at night, capacitive hand detection to avoid operating errors and easy-clean folding bellows for hygienically sensitive areas.

| Image/s: | joyscape_basic_und_ausbau | Characters: | 1,992 |
| --- | --- | --- | --- |
| File name: | 202101005_pm_joyscape-familie_als_oem-produkte_en | Date: | 01-13-2021 |

About the RAFI group

Founded in 1900, RAFI today develops and produces electromechanical components and systems for human–machine interaction. The range of products includes pushbuttons, switches, touchscreens, control systems and electronic assemblies. RAFI products are employed in many industries including automation, medical technology, machine and plant engineering, road and railway vehicles, household appliances and telecommunication. The RAFI group operates internationally with 2,000 employees at sites in Germany, Europe, China, and the USA. Its headquarters are in Berg, Germany.

| Contact: RAFI GmbH & Co. KG Artur Krug Ravensburger Str. 128–134 88276 Berg, Germany Phone: +49 751 89-1307 Fax: +49 751 89-1300 Email: artur.krug@rafi.de Internet: www.rafi.de |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin, Germany Phone: +49 30 53 89 65-0 Fax: +49 30 53 89 65-29 Email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |