Press Release

Demo kit helps select tried-and-tested IR sensors

A demo kit from manufacturer Excelitas facilitates the comparative evaluation of infrared temperature, motion, and presence detectors. The kit consists of an interface board, sensor adapters, and user-friendly software. The universal board easily connects a wide range of Excelitas IR sensors to developer PCs via a USB interface. This enables quick and reliable testing, allowing OEMs to make an informed decision about which sensors to integrate in their innovative smart devices and similar products. All basic parameters are accessible in the companion Windows software. That way, different types of sensors can be thoroughly examined. The demo kit supports both thermopile and pyroelectric sensors. Suitable adapter boards either feature sensor-specific sockets or, in the case of SMD products, they are supplied with sensors soldered onto the board. Presence and motion sensors provide key functions for many newly developed devices. Among other things, they enable the optimization of the energy efficiency of battery-powered products. Notably, low-power detectors such as Excelitas CaliPile have proven to be an ideal fit for battery-powered devices. In CaliPile series sensors, all detection functionality is handled by an integrated DSP, allowing the host device to stay in a power-saving sleep mode until a relevant event triggers a wake-up. For fast development of pure CaliPile applications, Excelitas also offers a simplified evaluation software specifically for this sensor family in addition to the comprehensive multi-sensor demo kit software.

Illustration: A demo kit from Excelitas with a universal interface board enables the quick and reliable selection of the best IR sensor for new, innovative devices

| Illustrations: | ir_sensing_application_kit | Char.s: | 1,560 |
| --- | --- | --- | --- |
| File name: | ENpm_2018_11-12_EXC_demo-kit-ir-sensors | Date: | 11-13-2018 |
| Tags: | 1 - DET - IR Sens | GPI: | 201811006 |

About Excelitas

Excelitas Technologies Corp. is a global technology leader focused on delivering innovative, high-performance, market-driven photonic solutions to meet the lighting, detection and optical technology needs of global customers. From biomedical technology to research laboratory, safety and security, consumer products, semiconductor, energy and environment, industrial sensing & imaging, defense and aerospace, Excelitas acquired Lumen Dynamics and Qioptiq in 2013 and now has approximately 6500 employees in North America, Europe and Asia, serving customers across the world.

| Contact: Excelitas Technologies Corp. Oliver Neutert Regional Marketing Manager EMEA Feldkirchen (near Munich) Germany Phone: +49 . 89 . 255 458-965 Email: oliver.neutert@excelitas.com Internet: www.excelitas.com |  | gii die Presse-Agentur GmbH Immanuelkirchstr. 12 10405 Berlin Germany Phone: +49 . 30 . 538 965-0 Email: info@gii.de Internet: www.gii.de |
| --- | --- | --- |